## Slide 1: thresholding

## Slide 2: thresholding
목적
  Object와 background의 구분
  Bimodal/multi modal image의 구분
상위 분류? – image segmentation

## Slide 3: 문제점/해결책?
Threshold가 어느 정도면 적절?
  자동으로 threshold 잡기 – otsu’s binarization
부분적으로 illumination이 다를 경우
  local 영역마다 threshold 다르게 – adaptive threshold
어쩔 수 없는 경우? ( histogram이 겹침 )
  hysterysis

## Slide 4: Simple thresholding
Cv2.threshold(image, threshold, maximum value, type)
  Image : 입력 image (uint8)
  Threshold : threshold 값
  Maximum value : THRESH_BINARY, THRESH_BINARY_INV에 사용되는 최대 값
  Thresholding 종류

## Slide 5: Threshold type

## Slide 6: Simple thresholding

## Slide 7: 결과

## Slide 8: Adaptive thresholding
Pixel마다 threshold를 구해서 적용
  Threshold : block의 평균 or weighted mean – C
주요 param : block size (홀수), C
특정 pixel threshold?
Pixel 근방 영역에서 계산
평균 / Gaussian kernel

## Slide 9: 함수
Cv2.AdaptiveThreshold(src, maxValue, adaptive_method, thresholdType, blockSize = 3, c[, dst])
  Src : 8 bit single channel image
  Adaptive method
    MEAN_C : Threshold value = mean of blocksize * block size of neighbore
    Gaussian_C : threshold value : weighted sum (cross-correlation with a Gaussian window ) . Default sigmal is used for specified blockSize. Sigma = 0.3 * ((ksize-1) * 0.5-1) + 0.8, ksize = odd
  C : constant subtracted from the mean or weighted mean

## Slide 10: code

## Slide 11: 결과

## Slide 12: Image에 적용 / block size
Original image
MEAN_C
GAUSSIAN_C
Block Size : 41
Block Size : 31

## Slide 13: Image에 적용 / C
C = 2
C = 10
MEAN_C
GAUSSIAN_C

## Slide 14: Image에 적용
항상 잘되는건 아님..

## Slide 15: Image에 적용 2
Block size와 C를 적절히 조절
어렵군요..
Block size 201, C = -100
배경 : 주변과 해당 pixel 사이 값이 유사. -> C를 크게 주면 됨
Block size 201, C = -51

## Slide 16: Otsu’s algorithm
To find a threshold value t which minimizes the weighted within-class variance
Histogram으로 plot
Threshold 기준 2 부분으로 나눔.
각 부분의 분산이 최소가 되는 threshold 찾음

## Slide 17: Otsu’s algorithm

## Slide 18: 함수
Cv2.threshold(src, threshold, maxvalue, cv2.THRESH_BINARY + cv2.THRESH_OTSU)

## Slide 21: Image에 적용

## Slide 22: 시도
Local threshold를 otsu로 계산
Block size = 51
Padding = 100

## Slide 23: hysterysis
주변 상황을 고려.
Canny edge detectio과 연관?
  High threshold, low threshold가 있음
  High threshold를 넘으면 edge
  Low threshold 아래면 edge가 아님
  중간에 있을 경우 주변에 edge가 있으면 edge, 아니면 아님.

## Slide 24: Image segmentation
process of partitioning a digital image into multiple segments
to simplify and/or change the representation of an image into something that is more meaningful and easier to analyze
to locate objects and boundaries (lines, curves, etc.) in images
image segmentation is the process of assigning a label to every pixel in an image such that pixels with the same label share certain characteristics